## Slide 1: Compositional Safety and Security Analysis of Architecture Models
Mike Whalen
Program Director University of Minnesota Software Engineering Center
Notes: 1

## Slide 2: Acknowledgements
Rockwell Collins (Darren Cofer, Andrew Gacek, Steven Miller, Lucas Wagner)
UPenn: (Insup Lee, Oleg Sokolsky)
UMN (Mats P. E. Heimdahl)
CMU SEI (Peter Feiler)

## Slide 3: Main Messages
We need a variety of reasoning approaches and partitioning methods for system-level requirements and analysis
Your How is My What: requirements vs. design is a often matter of perspective
Requirements hierarchies often follow system and software architectures.
Notes: What is the point of my talk?
- Your how is my what.

## Slide 4: Component Level Formal Analysis Efforts
Notes: Note: not a one man show! Collins continues to use this technology.

## Slide 6: Mismatched Assumptions
System Engineer
Control Engineer
Application Developer
System User
System
Under
Control
Control
System
Compute
Platform
Runtime
Architecture
Application
Software
Embedded SW System Engineer
Physical Plant Characteristics
Lag, proximity
Data Stream Characteristics
ETE Latency (F16)
State delta (NASA)
Measurement Units
Ariane 4/5
Air Canada
Concurrency Communication
ITunes crashes on dual-cores
Distribution & Redundancy
Virtualization of HW
(ARPA-Net split)
Operator Error
Lag, proximity
Hardware Engineer
Slide from: An Overview of AADL v2 by Peter Feiler, 2010

## Slide 7: Vision
System design & verification through pattern application and compositional reasoning
COMPUTING RESOURCE
SENSOR
LRU
FAIL-SILENT NODE FROM REPLICAS
COMPUTING RESOURCE A
COMPUTING RESOURCE B
VOTE MULTIPLE DATA
SENSOR 1
SENSOR 2
SENSOR 3
VERIFIED
AVAILABILITY
VERIFIED
INTEGRITY
ARCHITECTURE
MODEL
COMPOSITIONAL PROOF OF CORRECTNESS
(ASSUME – GUARANTEE)
SAFETY, BEHAVIORAL, PERFORMANCE PROPERTIES
ABSTRACTION
VERIFICATION
REUSE
COMPOSITION
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 8: Approach
PATTERN & COMP SPEC
LIBRARY
SYSTEM MODELING ENVIRONMENT
INSTANTIATE ARCH PATTERNS
& CHECK CONSTRAINTS
COMPOSITIONAL REASONING & ANALYSIS
SYSTEM MODEL
(AADL)
AUTO
GENERATE
SYSTEM IMPLEMENTATION
ARCH PATTERN MODELS
COMPONENT MODELS
ANNOTATE
& VERIFY MODELS
COMPONENT
LIBRARY
SPECIFICATION
SYSTEM DEVELOPMENT
FOUNDRY
Design Flow
Complexity-reducing design patterns
Capture best solutions to architectural design problems
Reuse of formally verified solutions
Increase level of design abstraction
2
Compositional verification
Reason about system behavior based on contracts and system design model structure
Compositional approach scales to large software systems
3
System architecture modeling
Apply formal specification and analysis tools to system-level design
Separate component specification and implementation
Automated model translation
1
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 9: Complexity-Reducing Architectural Design Patterns
Design pattern = model transformation
  p : M  M (partial function)
  Applied to system models
Reuse of verification is key
  Not software reuse
  Guaranteed behaviors associated with patterns (and components)
Reduce/manage system complexity
  Separation of concerns
  System logic vs. application logic (e.g., fault tolerance)
  Process complexity vs. design complexity
Encapsulate & standardize good solutions
  Raise level of abstraction
  Codify best practices
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 10: System Design Through Pattern Application
Avionics
System
Initial
System
Final
System
Pattern Application
System Hierarchy
Replicate
Leader Selection
PALS
Replicate
Active Standby Pattern
Flight
Control
Flight
Guidance
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 11: System verification
PATTERN & COMP SPEC
LIBRARY
SYSTEM MODELING ENVIRONMENT
INSTANTIATE ARCHITECTURAL PATTERNS
SYSTEM MODEL
AUTO
GENERATE
SYSTEM IMPLEMENTATION
ARCH PATTERN MODELS
COMPONENT MODELS
ANNOTATE
& VERIFY MODELS
COMPONENT
LIBRARY
SPECIFICATION
SYSTEM DEVELOPMENT
FOUNDRY
COMPOSITIONAL REASONING & ANALYSIS
Instantiation:
Check structural constraints, Embed assumptions & guarantees in system model
Compositional Verification:
System properties are verified by model checking using component & pattern contracts
Reusable Verification:
Proof of component and pattern requirements (guarantees) and specification of context (assumptions)
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 12: Hierarchical reasoning about systems
Avionics system requirement
Relies upon
  Accuracy of air data sensors
  Control commands from FCS
    Mode of FGS
    FGS control law behavior
    Failover behavior between FGS systems
    ….
  Response of Actuators
  Timing/Lag/Latency of Communications
FCS
Avionics
System
Under single-fault assumption, GC output transient response is bounded in time and magnitude
Autopilot
FGS_L
FGS_R
ADS_L
ADS_R
…
…
System Modes
Control Laws
Co-ord

## Slide 13: Compositional Reasoning for Active Standby
Want to prove a transient response property
  The autopilot will not cause a sharp change in pitch of aircraft.
  Even when one FGS fails and the other assumes control
Given assumptions about the environment
  The sensed aircraft pitch from the air data system is within some absolute bound and doesn’t change too quickly
  The discrepancy in sensed pitch between left and right side sensors is bounded.
and guarantees provided by components
  When a FGS is active, it will generate an acceptable pitch rate
As well as facts provided by pattern application
  Leader selection: at least one FGS will always be active (modulo one “failover” step)
transient_response_1 : assert true -> abs(CSA.CSA_Pitch_Delta) < CSA_MAX_PITCH_DELTA ;
transient_response_2 : assert true -> abs(CSA.CSA_Pitch_Delta - prev(CSA.CSA_Pitch_Delta, 0.0)) < CSA_MAX_PITCH_DELTA_STEP ;

## Slide 14: Hierarchical reasoning between analysis domains.
Avionics system requirement
Relies upon
  Guarantees provided by patterns and components
  Structural properties of model
  Resource allocation feasibility
  Probabilistic system-level failure characteristics
Platform
PALS
synchronous
communication
Replication
one node
operational
timing
constraints
not
co-located
Flight Control
System
Leader Selection
leader transition
managed on failure
ASSUMPTIONS
GUARANTEES
Under single-fault assumption, GC output transient response is bounded in time and magnitude
RT sched
& latency
Error
model
Behavior
Structure
Resource
Probabilistic
Principled mechanism for “passing the buck”
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 15: Contracts
Derived from Property Specification Language (PSL) formalism
  IEEE standard
  In wide use for hardware verification
Assume / Guarantee style specification
  Assumptions: “Under these conditions”
  Promises (Guarantees): “…the system will do X”
Local definitions can be created to simplify properties
Contract:
fun abs(x: real) : real = if (x > 0) then x else -x ;
const ADS_MAX_PITCH_DELTA: real = 3.0 ;
const FCS_MAX_PITCH_SIDE_DELTA: real = 2.0 ;
const CSA_MAX_PITCH_DELTA: real = 5.0 ;
const CSA_MAX_PITCH_DELTA_STEP: real = 5.0 ;
property AD_L_Pitch_Step_Delta_Valid =
true -> abs(AD_L.pitch.val - prev(AD_L.pitch.val, 0.0)) < ADS_MAX_PITCH_DELTA ;
property AD_R_Pitch_Step_Delta_Valid =
true -> abs(AD_R.pitch.val - prev(AD_R.pitch.val, 0.0)) < ADS_MAX_PITCH_DELTA ;
property Pitch_lr_ok =
abs(AD_L.pitch.val - AD_R.pitch.val) < FCS_MAX_PITCH_SIDE_DELTA ;
property some_fgs_active =
(FD_L.mds.active or FD_R.mds.active) ;
active_assumption: assume some_fgs_active ;
transient_assumption :
assume AD_L_Pitch_Step_Delta_Valid and
AD_R_Pitch_Step_Delta_Valid and Pitch_lr_ok ;
transient_response_1 :
assert true -> abs(CSA.CSA_Pitch_Delta) < CSA_MAX_PITCH_DELTA ;
transient_response_2 :
assert true -> abs(CSA.CSA_Pitch_Delta - prev(CSA.CSA_Pitch_Delta, 0.0)) < CSA_MAX_PITCH_DELTA_STEP ;
© Copyright 2011 Rockwell Collins, Inc.
All rights reserved.

## Slide 16: Reasoning about contracts
Notionally: It is always the case that if the component assumption is true, then the component will ensure that the guarantee is true.
  G(A  P);
An assumption violation in the past may prevent component from satisfying current guarantee, so we need to assert that the assumptions are true up to the current step:
  G(H(A)  P) ;

## Slide 17: Systems of Contracts
Architectures are hierarchically composed in layers.
  Visually: a box and line diagram
  Formally you can view a layer as a system S: S = (A, P, C)
    C is a finite set of component contracts C: ℙ (A x P)

## Slide 18: Reasoning about Contracts
Given the set of component contracts: Γ = { G(H(Ac)  Pc) | c ∈ C }
Architecture adds a set of obligations that tie the system assumption to the component assumptions
This process can be repeated for any number of abstraction levels

## Slide 19: Composition Formulation
Suppose we have
Then if for all q ∈ Q
  Γ  G((Z(H(Θq)) ^ Δq)  q)
Then: G(q) for all q ∈ Q
[Adapted from McMillan]

## Slide 20: A concrete example
Order of data flow through system components is computed by reasoning engine
  {System inputs}  {FGS_L, FGS_R}
  {FGS_L, FGS_R}  {AP}
  {AP}  {System outputs}
Based on flow, we establish four proof obligations
  System assumptions  FGS_L assumptions
  System assumptions  FGS_R assumptions
  System assumptions + FGS_L guarantees + FGS_R guarantees  AP assumptions
  System assumptions + {FGS_L, FGS_R, AP} guarantees  System guarantees
System can also handle circular flows, but user has to choose where to break cycle

## Slide 21: Architecture of Generic Infusion Pump
GPCA = Generic Patient-Controlled Analgesia
Product Family architecture
GPCA Pump
Pump Hardware
Flow Rate Detector
Door
Pump Position
Humidity
Temp
Air Pressure
Battery
Power Supply
Air In Line Detector
Pump Motor
Buzzer
Pump Controller Software
Infusion Command

## Slide 22: GPCA Pump Example
Property of Interest:
  If a “Pump Stop” command is received, then within 1 second, measured flow rate shall be zero.
We will prove this property compositionally based on the architecture of the Pump subsystem.
With
exciting verification
demo!

## Slide 23: Proof of GPCA Pump
GPCA Pump
Pump Hardware
Flow Rate Detector
Pump Position
Humidity
Temp
Battery
Power Supply
Pump Motor
Buzzer
Pump Controller Software
Infusion Command
Assertion: When a “Pump Stop” infusion command is received, then within 1 second, measured flow rate shall be zero.
…
…
…

## Slide 24: Proof of Reciprocating Pump
GPCA Pump
Reciprocating Pump Hardware
Flow Rate Detector
Humidity
Temp
Battery
Power Supply
Pump Motor
Buzzer
Pump Controller Software
Assertion: When a “Pump Stop” infusion command is received, then within 1 second, measured flow rate shall be zero.
When pump stop command occurs, pump motor will be switched off when pump motor position reaches no-ambient flow state.
Door
Assertion: When powered on, pump cycles between ambient and no-ambient flow states every 300 ms.
if pump is in no ambient flow position and pump motor is off, then flow rate will be zero within 200 ms

## Slide 25: Proof of Rotary Pump
GPCA Pump
Rotary Pump Hardware
Flow Rate Detector
Humidity
Temp
Battery
Power Supply
Pump Motor
Buzzer
Pump Controller Software
Assertion: When a “Pump Stop” infusion command is received, then within 1 second, measured flow rate shall be zero.
When pump stop command occurs, pump motor will be immediately switched off.
Door
if pump is in no ambient flow position and pump motor is off, then flow rate will be zero within 400 ms

## Slide 26: Architecture and Requirements

## Slide 27: Requirements or Design Information?
The patient shall never be infused with a single air bubble more than 5ml volume.
When a single air bubble more than 5ml volume is detected, the system shall stop infusion within 0.01 seconds.
When a single air bubble more than 5ml volume is detected, the system shall issue an air-embolism command.
When air-embolism command is true, the system shall stop infusion.
When air-embolism command is received, the system shall stop piston movement within 0.1 second.

## Slide 28: A: Both
The patient shall never be infused with a single air bubble more than 5ml volume.
When a single air bubble more than 5ml volume is detected, the system shall stop infusion within 0.01 seconds.
When a single air bubble more than 5ml volume is detected, the system shall issue an air-embolism command.
When air-embolism command is true, the system shall stop infusion.
When air-embolism command is received, the system shall stop piston movement within 0.1 seconds
PATIENT THERAPY SYSTEM
INFUSION SYSTEM
AIR BUBBLE SENSOR
DRUG DELIVERY HARDWARE
PUMP SYSTEM
PUMP HARDWARE
PUMP CONTROLLER

## Slide 30: Your How is My What
Systems are hierarchically organized
Requirements vs. architectural design must be a matter of perspective
Need better support for N-level decompositions for requirements and architectural design
  Reference model support
    How do elements “flow” between world, machine, and specification as we decompose systems?
  Certification standard support (DO-178B/C)
    Currently: two levels of decomposition: “high” and “low”

## Slide 31: Twin Peaks

## Slide 32: Often, Architecture Comes First
Candidate architectures from previous systems
  Designer familiarity
  Cost amortization
Program families
Certification or criticality requirements
Architectural choices often restrict set of achievable system requirements.

## Slide 33: Flow is Bi-directional

## Slide 34: Requirements Validation and Verification
Given hierarchical systems, where are the most serious problems with requirements?
  At the component level?
  At the top-level?
  Somewhere in the middle?
A hypothesis:
  The most problematic are the layers in the middle
  Errors in decomposing system requirements become integration problems.
These are requirements to be both verified and validated.

## Slide 35: Structural Properties

## Slide 36: Structural Properties
Often, we are interested in properties about a model structure
  Given the processor resources, is the system schedulable?
  Is my software correctly distributed across different physical resources?
  Are my end-to-end timing assumptions met?
Often these involve checking the mapping between the software and the hardware.

## Slide 37: Structural Properties
Software + HW platform
  Process, thread, processors, bus
Ex: PALS vertical contract
  PALS timing constraints on platform
  Check AADL structural properties
Guarantees
  Sync logic executes at PALS_Period
  Synchronous_Communication
  => “One_Step_Delay”
Assumptions (about platform)
  Causality constraint:
  Min(Output time) ≥ 2ε – μmin
  PALS period constraint:
  Max(Output time) ≤ T - μmax - 2ε
Software
Platform

## Slide 38: PALS assumptions in AADL
Compute_Execution_Time
Latency
Ti
Ti+1
( ± )
( ± )
Output
message
Input
message
available
Period
Deadline
Dispatch_Offset (if imposed)
Dispatch_Jitter (if describing max scheduling delay)
Output_Time
Clock_Jitter
Thread execution
( ±)
Latest period start on other node
Earliest output message
Min(Output_Time)
Min(Latency)
Causality Constraint
Thread execution
Max(Latency)
( ±)
( ±)
Latest output
message
Deadline
Latest period start
Earliest period start on other node
Period
Max(Output_Time)
PALS Period Constraint

## Slide 39: Structural property checks
Contract
  Platform model satisfies PALS assumptions
Attached at pattern instantiation
  Model-independent
  Assumptions
  Pre/post-conditions
Lute theorems
  Based on REAL
  Eclipse plug-in
  Structural properties in AADL model
PALS_Threads := {s in Thread_Set | Property_Exists(s, "PALS_Properties::PALS_Id")};
PALS_Period(t) := Property(t, "PALS_Properties::PALS_Period");
PALS_Id(t) := Property(t, "PALS_Properties::PALS_Id");
PALS_Group(t) := {s in PALS_Threads | PALS_Id(t) = PALS_Id(s)};
Max_Thread_Jitter(Threads) :=
Max({Property(p, "Clock_Jitter") for p in Processor_Set |
Cardinal({t in Threads | Is_Bound_To(t, p)}) > 0});
Connections_Among(Set) :=
{c in Connection_Set | Member(Owner(Source(c)), Set) and
Member(Owner(Destination(c)), Set)};
theorem PALS_Period_is_Period
foreach s in PALS_Threads do
check Property_Exists(s, "Period") and
PALS_Period(s) = Property(s, "Period");
end;
theorem PALS_Causality
foreach s in PALS_Threads do
PALS_Group := PALS_Group(s);
Clock_Jitter := Max_Thread_Jitter(PALS_Group);
Min_Latency := Min({Lower(Property(c, "Latency")) for
c in Connections_Among(PALS_Group)});
Output_Delay := {Property(t, "Output_Delay") for t in PALS_Group};
check (if 2 * Clock_Jitter > Min_Latency then
Min(Output_Delay) > 2 * Clock_Jitter - Min_Latency
else
true);
end;

## Slide 40: Tool Chain
AADL
SysML-AADL translation
EDICT:
Architectural
patterns
Lute:
Structural
verification
AGREE:
Compositional behavior verification
OSATE:
AADL modeling
Enterprise Architect
Eclipse
KIND
SysML
Lustre

## Slide 41: Research Challenges

## Slide 42: Structural and Behavioral Properties
Theorem RMA
foreach e in Processor_Set do
Proc_Set(e) := { x in Process_Set | Is_Bound_To(x, e) } ;
Threads := { x in Thread_Set | Is_Subcomponent_Of(x, Proc_Set) }
check (sum (get_property_value (Threads “RTOS_properties::Utilization”)) <= (Cardinal (Threads) * (2 ** (1 / Cardinal (Threads))) -1 ) ) ;
End RMA ;
Assertion: My system is schedulable using Rate Monotonic Scheduling.
Assertion: If a “Pump Stop” command is received, then within 1 second the measured flow rate shall be zero.
PSL_contract
property no_flow_after_stop : after (not (infusion_control_in.Pump_On)) (exists flow_rate_detector_out.Rate = 0 within STEPS_PER_SECOND *1) ;
assert (no_flow_after_stop) ;
end PSL_contract;
Checkable with Lute
Checkable with AGREE
Structural (Non-functional) Properties: Analyze conformance, optimization properties for hardware resources and model structure.
Behavioral (functional) Properties: Analyze system behavior. Behavioral properties may use structural properties.

## Slide 43: Are these the “right” logics?
Simpler logics have benefits
  Primary benefit: much simpler to analyze
  AADL error annex is (mostly) propositional
    Makes analysis simpler
    Supports useful categorization of errors
  Datalog-style logics support “timeless” analysis
    The Lute checker is essentially a datalog interpreter
More complicated logics are necessary for certain properties
  Richer types (e.g., algebraic types for XML messages)
  Quantification

## Slide 44: Dealing with Time
Pure synchrony or asynchrony
Uniform discrete time
  Choose fixed time quantum between steps
  This quantum need not be the same between layers
  Adjust process behavior and requirements with clocks.
Non-uniform discrete time
  Calendar/Timeout automata advance system to next interesting instant
Dense time
MOST ACCURATE
SIMPLEST

## Slide 45: Scaling
What do you do when systems and subcomponents have hundreds of requirements?
  FGS mode logic: 280 requirements
  DWM: >600 requirements
Need to create automated slicing techniques for predicates rather than code.
  Perhaps this will be in the form of counterexample-guided refinement

## Slide 46: Assigning blame
Counterexamples are often hard to understand for big models
It is much worse (in my experience) for property- based models
Given a counterexample, can you automatically assign blame to one or more subcomponents?
Given a “blamed” component, can you automatically open the black box to strengthen the component guarantee?
Signal | Step... |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5
AD_L.pitch.val | -0.91 | -1.83 | -2.74 | -3.65 | -4.35 | -4.39
AD_L.pitch.valid | FALSE | TRUE | FALSE | TRUE | TRUE | FALSE
AD_R.pitch.val | 0.83 | -0.09 | -1.00 | -1.91 | -2.83 | -3.74
AD_R.pitch.valid | TRUE | FALSE | TRUE | FALSE | FALSE | TRUE
AP.CSA.csa_pitch_delta | 0.00 | 0.13 | 0.09 | 0.26 | 0.74 | -4.26
AP.GC_L.cmds.pitch_delta | 0.00 | -4.91 | -4.65 | -4.57 | -4.74 | -4.35
AP.GC_L.mds.active | TRUE | FALSE | FALSE | FALSE | FALSE | TRUE
AP.GC_R.cmds.pitch_delta | 0.00 | 0.83 | -4.43 | -4.48 | 4.91 | 4.83
AP.GC_R.mds.active | TRUE | TRUE | FALSE | FALSE | FALSE | FALSE
Assumptions for AP | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE
Assumptions for FCI | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE
Assumptions for FGS_L | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE
Assumptions for FGS_R | TRUE | TRUE | TRUE | TRUE | TRUE | TRUE
FGS_L.GC.cmds.pitch_delta | -4.91 | -4.65 | -4.57 | -4.74 | -4.35 | 0.09
FGS_L.GC.mds.active | FALSE | FALSE | FALSE | FALSE | TRUE | FALSE
FGS_L.LSO.leader | 2 | 2 | 3 | 2 | 1 | 3
FGS_L.LSO.valid | FALSE | TRUE | FALSE | TRUE | TRUE | FALSE
FGS_R.GC.cmds.pitch_delta | 0.83 | -4.43 | -4.48 | 4.91 | 4.83 | 3.91
FGS_R.GC.mds.active | TRUE | FALSE | FALSE | FALSE | FALSE | FALSE
FGS_R.LSO.leader | 0 | 0 | 1 | 0 | 1 | 1
FGS_R.LSO.valid | TRUE | FALSE | TRUE | FALSE | FALSE | TRUE
leader_pitch_delta | 0.00 | 0.83 | 0.83 | 0.83 | 0.83 | -4.35
System level guarantees | TRUE | TRUE | TRUE | TRUE | TRUE | FALSE
Notes: Counterexamples can be hard to figure out when you have a functional system. They are much harder to understand (in my experience) when doing these compositional proofs.

## Slide 47: “Argument Engineering”
Disparate kinds of evidence throughout the system
  Probabilistic
  Resource
  Structural properties of model
  Behavioral properties of model
How do we tie these things together?
Evidence graph, similar to proof graph in PVS
  Shows evidential obligations that have not been discharged
SRI is working on this: Evidential Tool Bus (ETB)
  This seems to be a reasonable approach for tying tool results together
  Declarative (like make or ant), but more powerful (uses Datalog)

## Slide 48: Integration with AADL
Type representations
  Currently we use “homebrew” property set for typing information
  AADL data modeling annex?
Inheritance and Refinement
  Extends from same AADL class
  Implements from different AADL class
  Contracts should preserve behavioral subtyping
    Weaken assumptions
    Strengthen guarantees
  Some subtleties:
    For existential properties over traces (CTL), this refinement is generally unsound.
    Probably only want to support universal properties (like LTL)
Binding of logical system to physical system
  Contracts are built on many assumptions involving physical system involving resources. Currently these are not addressed in the temporal logic, but externally
  How do we represent physical failures in logical contracts?

## Slide 49: Conclusions
AADL is very nice for designing systems
  Good way to describe hardware and software
  Lots of built-in analysis capabilities
Allows new system engineering approaches
  Iteration between reqs and design
  Specification and use of architectural patterns
Looking at behavioral and structural analysis
  Still lots of work to do!
  ..but already can do some interesting analysis with tools
  Sits in a nice intersection between requirements engineering and formal methods
  Starting to apply this to large UAV models for security properties in the SMACCM project

## Slide 50: System Architectural Modeling & Analysis
System Architecture Development
Software Component Development

## Slide 51: Thank you!